## Slide 1
Digital Image Processing
Chapter # 3
Image Transformations and Spatial Filtering

## Slide 2: Image Enhancement
2
Notes: 2

## Slide 3: Image Enhancement
3
Notes: 3

## Slide 4: Image Enhancement
4
Image Enhancement Methods
  Spatial Domain: Direct manipulation of pixels in an image
  Transform Domain: Transform the image to some other domain, do the processing and apply inverse transform
Process an image so that the result is more suitable than the original image for a specific application
This Chapter – Spatial Domain
Notes: 4

## Slide 5: Types of image enhancement operations
5
Point/Pixel operations
Output value at specific coordinates (x,y) is dependent only on the input value at (x,y)
Local operations
The output value at (x,y) is dependent on the input values in the neighborhood of (x,y)
Global operations
The output value at (x,y) is dependent on all the values in the input image
Notes: 5

## Slide 6: Basic Concepts
6
Most spatial domain enhancement operations can be generalized as:
f (x, y) = the input image
g (x, y) = the processed/output image
T = some operator defined over some neighbourhood of (x, y)
Notes: 6

## Slide 7: Basic Concepts
7
A square or rectangular sub-image area centered at (x,y)
Origin
x
y
Image f (x, y)
(x, y)
Notes: 7

## Slide 8: Point Processing
8
In a digital image, point = pixel
Point processing transforms a pixel’s value as function of its value alone;
It does not depend on the values of the pixel’s neighbors.
Notes: 8

## Slide 9: Point Processing
9
Neighborhood of size 1x1:
g depends only on f at (x,y)
T: Gray-level/intensity transformation/ mapping function
  r = gray level of f at (x,y)
  s = gray level of g at (x,y)
Notes: 9

## Slide 10: Point Processing using Look-up Tables
10
0
127
255
0
127
255
input value
output value
index
value
...
101
102
103
104
105
106
...
...
64
68
69
70
70
71
...
E.g.:
input
output
A look-up table (LUT) implements a functional mapping.
Notes: 10

## Slide 11: Point Processing using Look-up Tables
11
cell index
contents
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
input
output
a pixel with this value
is mapped to this value
Notes: 11

## Slide 12: Point Processing Transformations
12
There are many different kinds of grey level transformations
Three of the most common are shown here
  Linear
    Negative/Identity
  Logarithmic
    Log/Inverse log
  Power law
    nth power/nth root
Notes: 12

## Slide 13: Point Processing Example: Negative Images
13
Reverses the gray level order
For L gray levels, the transformation has the form:
Negative images are useful for enhancing white or grey detail embedded in dark regions of an image
Notes: 13

## Slide 14: Point Processing Example: Negative Images
14
Notes: 14

## Slide 15: Point Processing Example: Intensity Scaling
15
Notes: 15

## Slide 16: Point Processing Example: Thresholding
16
Segmentation of an object of interest from a background
s =
1.0
0.0
r <= threshold
r > threshold
Notes: 16

## Slide 17
17
s =
0.0 r <= threshold
1.0 r > threshold
Point Processing Example: Thresholding
Notes: 17

## Slide 18: Logarithmic Transformations
18
The general form of the log transformation is
The log transformation maps a narrow range of low input grey level values into a wider range of output values
The inverse log transformation performs the opposite transformation
Notes: 18

## Slide 19: Logarithmic Transformations
19
Properties
  For lower amplitudes of input image the range of gray levels is expanded
  For higher amplitudes of input image the range of gray levels is compressed
Notes: 19

## Slide 20: Logarithmic Transformations
20
Application
  This transformation is suitable for the case when the dynamic range of a processed image far exceeds the capability of the display device (e.g. display of the Fourier spectrum of an image)
  Also called “dynamic-range compression / expansion”
Notes: 20

## Slide 21: Logarithmic Transformations
21
Fourier spectrum: image values ranging from 0 to 1.5x106
The result of log transformation with c = 1
Notes: 21

## Slide 22: Power Law Transformations
22
Power law transformations have the following form
Map a narrow range of dark input values into a wider range of output values or vice versa
Varying γ gives a whole family of curves
Notes: 22

## Slide 23: Power Law Transformations
23
For g< 1: Expands values of dark pixels, compress values of brighter pixels
For g > 1: Compresses values of dark pixels, expand values of brighter pixels
If g=1 & c=1: Identity transformation (s = r)
A variety of devices (image capture, printing, display) respond according to a power law and need to be corrected
Gamma (g) correction
The process used to correct the power-law response phenomena
Notes: 23

## Slide 24: Power Law Transformations: Gamma Correction
24
Notes: 24

## Slide 25: Power Law Transformations Contrast Enhancement
25
The images to the right show a magnetic resonance (MR) image of a fractured human spine
Notes: 25

## Slide 26: Power Law Transformations Contrast Enhancement
26
γ = 0.6
Notes: 26

## Slide 27: Power Law Transformations Contrast Enhancement
27
γ = 0.4
Notes: 27

## Slide 28: Power Law Transformations Contrast Enhancement
28
γ = 0.3
Notes: 28

## Slide 29: Power Law Transformations Contrast Enhancement
29
MR image of
fractured human spine
Result after
Power law transformation
c = 1, g = 0.6
Result after
Power law transformation
c = 1, g = 0.4
Result after
Power law transformation
c = 1, g = 0.3
Notes: 29

## Slide 30: Power Law Transformations Contrast Enhancement
30
When the γ is reduced too
much, the image begins to
reduce contrast to the
point where the image
started to have very slight
“wash-out” look.
Notes: 30

## Slide 31: Power Law Transformations Contrast Enhancement
31
Image has a washed-out
appearance – needs γ > 1
Notes: 31

## Slide 32: Image Enhancement
32
Aerial
Image
Result of
Power law transformation
c = 1, g = 3.0
(suitable)
Result of Power law transformation
c = 1, g = 4.0
(suitable)
Result of
Power law transformation
c = 1, g = 5.0
(high contrast, some regions are too dark)
Notes: 32

## Slide 33: Piecewise Linear Transformation Functions
33
Contrast stretching
Intensity level slicing
Bit-Plane slicing
Notes: 33

## Slide 34: Contrast Stretching
34
Objective
  Increase the dynamic range of the gray levels for low contrast images
Rather than using a well defined mathematical function we can use arbitrary user-defined transforms
If r1 = s1 & r2 = s2, no change in gray levels
If r1 = r2, s1 = 0 & s2 = L-1, then it is a threshold function. The resulting image is binary
Notes: 34

## Slide 35: Contrast Stretching
35
r1 = rmin & s1 = 0
r2 = rmax & s2 = L-1
Notes: 35

## Slide 36: Contrast Stretching
36
Notes: 36

## Slide 37: Grey Level Slicing
37
Highlights a specific range of gray levels in an image
  Similar to thresholding
  Other levels can be suppressed or maintained
  Useful for highlighting features in an image
Notes: 37

## Slide 38: Grey Level Slicing
38
Highlights range [A,B] but preserves all other gray levels
Highlights range [A,B] of gray levels and reduces all others to a contrast level
Notes: 38

## Slide 39: Grey Level Slicing
39
Notes: 39

## Slide 40: Bit Plane Slicing
40
Objective: Highlights the contribution made to the image appearance by specific bits
Suppose an image is of 8 bits i.e. each pixel is represented by 8 bits
Higher-order bits contain the majority of the visually significant data
Useful for analyzing the relative importance played by each bit of the image. It is useful in compression
Notes: 40

## Slide 41: Bit Plane Slicing
41
Notes: 41

## Slide 42: Image Enhancement
42
[10000000]
[01000000]
[00100000]
[00001000]
[00000100]
[00000001]
Notes: 42

## Slide 43: Bit Plane Slicing
43
Bit planes 1 through 8
Notes: 43

## Slide 44: Bit Plane Slicing
44
Reconstructed image using only bit planes 8 and 7
Reconstructed image using only bit planes 8, 7 and 6
Reconstructed image using only bit planes 7, 6 and 5
Notes: 44

## Slide 45: Histogram of a Grayscale Image
45
Let I be a 1-band (grayscale) image.
I(r,c) is an 8-bit integer between 0 and 255.
Histogram, hI, of I:
  a 256-element array, hI
  hI (g) = number of pixels in I that have value g.
    for g = 0,1, 2, 3, …, 255
Notes: 45

## Slide 46: Histogram of a Grayscale Image
46
Histogram of a digital image with gray levels in the range [0,L-1] is a discrete function
Where
  rk = kth gray level
  nk = number of pixels in the image having gray level rk
  h(rk) = histogram of an image having rk gray levels
Notes: 46

## Slide 47: Normalized Histogram
47
Dividing each of histogram at gray level rk by the total number of pixels in the image, n
p(rk) gives an estimate of the probability of
occurrence of gray level rk
The sum of all components of a normalized
histogram is equal to 1
Notes: 47

## Slide 48: Histogram of a Grayscale Image
48
16-level (4-bit) image
black marks pixels with intensity g
lower RHC: number of pixels with intensity g
Notes: 48

## Slide 49: Histogram of a Grayscale Image
49
Plot of histogram:
number of pixels with intensity g
Black marks pixels with intensity g
Notes: 49

## Slide 50: Histogram of a Grayscale Image
50
Plot of histogram:
number of pixels with intensity g
Black marks pixels with intensity g
Notes: 50

## Slide 51: Histogram of a Color Image
51
If I is a 3-band image
then I(r,c,b) is an integer between 0 and 255.
I has 3 histograms:
  hR(g) = # of pixels in I(:,:,1) with intensity value g
  hG(g) = # of pixels in I(:,:,2) with intensity value g
  hB(g) = # of pixels in I(:,:,3) with intensity value g
Notes: 51

## Slide 52: Histogram of a Color Image
52
There is one histo-gram per color band
R, G, & B. Luminosity histogram is from 1 band = (R+G+B)/3
Notes: 52

## Slide 53: Histogram of a Color Image
53
Notes: 53

## Slide 54: Histogram of a Color Image
54
Notes: 54

## Slide 55: Histogram: Example
55
How would the histograms of these images look like?
Dark Image
Bright Image
Notes: 55

## Slide 56: Histogram: Example
56
Dark image
Components of
histogram are
concentrated on the low side of the gray scale
Bright image
Components of
histogram are
concentrated on the high side of the gray scale
Notes: 56

## Slide 57: Histogram: Example
57
How would the histograms of these images look like?
Low Contrast Image
High Contrast Image
Notes: 57

## Slide 58: Histogram: Example
58
Low contrast image
Histogram is narrow and centered toward the middle of the gray scale
High contrast image
Histogram covers broad range of the gray scale and the distribution of pixels is not too far from uniform with very few
vertical lines being much higher than the others
Notes: 58

## Slide 59: Contrast Stretching
59
Improve the contrast in an image by `stretching' the range of intensity values it contains to span a desired range of values, e.g. the the full range of pixel values
Notes: 59

## Slide 60: Contrast Stretching
60
If rmax and rmin are the maximum and minimum gray level of the input image and L is the total gray levels of output image, the transformation function for contrast stretch will be
0
127
255
0
127
255
rmin
L
rmax
Notes: 60

## Slide 61: Contrast Stretching
61
Notes: 61

## Slide 62: Histogram Equalization
62
Histogram equalization re-assigns the intensity values of pixels in the input image such that the output image contains a uniform distribution of intensities
Notes: 62

## Slide 63: The Probability Distribution Function of an Image
63
This is the probability that an arbitrary pixel from I has value g.
Notes: 63

## Slide 64: The Probability Distribution Function of an Image
64
p(g) is the fraction of pixels in an image that have intensity value g.
p(g) is the probability that a pixel randomly selected from the given image has intensity value g.
Whereas the sum of the histogram h(g) over all g from 0 to 255 is equal to the number of pixels in the image, the sum of p(g) over all g is 1.
p is the normalized histogram of the image
Notes: 64

## Slide 65: The Cumulative Distribution Function of an Image
65
This is the probability that any given pixel from I has value less than or equal to g.
Let q = I(r,c) be the value of a randomly selected pixel from I. Let g be a specific gray level. The probability that q ≤ g is given by
where hI(γ ) is the histogram of image I.
Notes: 65

## Slide 66: The Cumulative Distribution Function of an Image
66
This is the probability that any given pixel from I has value less than or equal to g.
Let q = I(r,c) be the value of a randomly selected pixel from I. Let g be a specific gray level. The probability that q ≤ g is given by
where hI(γ ) is the histogram of image I.
Also called CDF for “Cumulative Distribution Function”.
Notes: 66

## Slide 67: The Cumulative Distribution Function of an Image
67
P(g) is the fraction of pixels in an image that have intensity values less than or equal to g.
P(g) is the probability that a pixel randomly selected from the given band has an intensity value less than or equal to g.
P(g) is the cumulative (or running) sum of p(g) from 0 through g inclusive.
P(0) = p(0) and P(255) = 1;
Notes: 67

## Slide 68: Histogram Equalization
68
The CDF itself is used as the LUT.
be the cumulative (probability) distribution function of I.
Task: remap image I so that its histogram is as close to constant as possible
Notes: 68

## Slide 69: Histogram Equalization
69
pdf
The CDF (cumulative distribution) is the LUT for remapping.
CDF
Notes: 69

## Slide 70: Histogram Equalization
70
pdf
The CDF (cumulative distribution) is the LUT for remapping.
LUT
Notes: 70

## Slide 71: Histogram Equalization
71
pdf
The CDF (cumulative distribution) is the LUT for remapping.
LUT
Notes: 71

## Slide 72: Histogram Equalization
72
Notes: 72

## Slide 73: Histogram Equalization
73
after
before
Luminosity
Notes: 73

## Slide 74: Histogram Equalization: Example
74
An 8x8 image
Notes: 74

## Slide 75: Histogram Equalization: Example
75
Image Histogram (Non-zero values)
Fill in the following table/histogram
Notes: 75

## Slide 76: Histogram Equalization: Example
76
Image Histogram (Non-zero values shown)
Notes: 76

## Slide 77: Histogram Equalization: Example
77
Notes: 77

## Slide 78: Histogram Equalization: Example
78
Cumulative Distribution Function (cdf)
Image Histogram/Prob Mass Function
Notes: 78

## Slide 79: Histogram Equalization: Example
79
Cumulative Distribution Function (cdf)
Notes: 79

## Slide 80: Histogram Equalization: Example
80
Cumulative Distribution Function (cdf)
Notes: 80

## Slide 81: Histogram Equalization: Example
81
Normalized Cumulative Distribution Function (cdf)
Divide each value by total number of pixels (64) to get the normalized cdf
Notes: 81

## Slide 82: Histogram Equalization: Example
82
Original Image
 |  |  |  |  |  | 183 | 
If cdf is normalized
If cdf is NOT normalized
Notes: 82

## Slide 83: Histogram Equalization: Example
83
Notes: 83

## Slide 84: Histogram Equalization: Example
84
Original Image
Corresponding histogram (red) and cumulative histogram (black)
Image after histogram equalization
Corresponding histogram (red) and cumulative histogram (black)
Notes: 84

## Slide 85: Histogram Equalization: Example
85
Dark image
Bright image
Equalized Histogram
Equalized Histogram
Notes: 85

## Slide 86: Histogram Equalization: Example
86
Low contrast
High Contrast
Equalized Histogram
Equalized Histogram
Notes: 86

## Slide 87: Histogram Equalization vs. Contrast Stretching
Histogram equalization is sophisticated version of contrast stretching
Contrast Stretching – Enhancement is less harsh

## Slide 88: Histogram Equalization vs. Contrast Stretching
Original Image
Contrast Stretching
Histogram Equalization
Dramatic Enhancement - Artificial look

## Slide 89: Histogram Equalization vs. Contrast Stretching
Original Image
Contrast Stretching
Histogram Equalization

## Slide 90: Spatial Filtering

## Slide 91: Spatial Filtering
91
Notes: 91

## Slide 92: Spatial Filtering
92
Notes: 92

## Slide 93: Spatial Filtering: Basics
93
Neighbourhood operations: Operate on a larger neighbourhood of pixels than point operations
Origin
x
y
Image f (x, y)
(x, y)
Neighbourhood
Neighbourhoods are mostly a rectangle around a central pixel
Notes: 93

## Slide 94: Spatial Filtering: Basics
94
123
127
128
119
115
130
140
145
148
153
167
172
133
154
183
192
194
191
194
199
207
210
198
195
164
170
175
162
173
151
Original Image
x
y
Enhanced Image
x
y
Notes: 94

## Slide 95: Spatial Filtering: Basics
95
r
s
t
u
v
w
x
y
z
Origin
x
y
Image f (x, y)
eprocessed = v*e + r*a + s*b + t*c + u*d + w*f + x*g + y*h + z*i
Filter
Simple 3*3 Neighbourhood
e
3*3 Filter
a
b
c
d
e
f
g
h
i
Original Image Pixels
*
The above is repeated for every pixel in the original image to generate the filtered image
Notes: 95

## Slide 96: Spatial Filtering: Basics
96
Moving window (kernel) scans the 3x3 neighborhood of every pixel in the image
Original Image
Notes: 96

## Slide 97: Spatial Filtering: Basics
97
Notes: 97

## Slide 98: Spatial Filtering: Basics
98
Notes: 98

## Slide 99: Spatial Filtering: Basics
99
Notes: 99

## Slide 100: Spatial Filtering: Basics
100
Notes: 100

## Slide 101: Spatial Filtering: Basics
101
Notes: 101

## Slide 102: Spatial Filtering: Basics
102
Mask operation near the image border: Problem arises when part of the mask is located outside the image plane
Discard the problem pixels (e.g. 512x512 input 510x510 output if mask size is 3x3)
Zero padding: Expand the input image by padding zeros (512x512 original image, 514x514 padded image, 512x512 output)
  Zero padding is not recommended as it creates artificial lines or edges on the border
Pixel replication: We normally use the gray levels of border pixels to fill up the expanded region (for 3x3 mask). For larger masks a border region equal to half of the mask size is mirrored on the expanded region.
Notes: 102

## Slide 103: Mask operation near the border: Pixel replication
103
Notes: 103

## Slide 104: Spatial Filtering: Basics
104
The output intensity value at (x,y) depends not only on the input intensity value at (x,y) but also on the specified number of neighboring intensity values around (x,y)
Spatial masks (also called window, filter, kernel, template) are used and convolved over the entire image for local enhancement (spatial filtering)
The size of the masks determines the number of neighboring pixels which influence the output value at (x,y)
The values (coefficients) of the mask determine the nature and properties of enhancing technique
Notes: 104

## Slide 105: Spatial Filtering: Basics
105
Filtering can be given in equation form as shown above
Notes: 105

## Slide 106: Spatial Filtering: Basics
106
Given the 3×3 mask with coefficients: w1, w2,…, w9
The mask cover the pixels with gray levels: z1, z2,…, z9
z gives the output intensity value for the processed image (to be stored in a new array) at the location of z5 in the input image
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
w1 | w2 | w3
w4 | w5 | w6
w7 | w8 | w9
Notes: 106

## Slide 107: Smoothing Spatial Filters
107
For blurring/noise reduction
Blurring is usually used in preprocessing steps, e.g., to remove small details from an image prior to object extraction, or to bridge small gaps in lines or curves
Equivalent to Low-pass spatial filtering in frequency domain because smaller (high frequency) details are removed based on neighborhood averaging (averaging filters)
Notes: 107

## Slide 108: Smoothing Spatial Filters
108
Simply average all of the pixels in a neighbourhood around a central value
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
Simple averaging filter
Notes: 108

## Slide 109: Spatial Filtering: Basics
109
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
Origin
x
y
Image f (x, y)
e = 1/9*106 + 1/9*104 + 1/9*100 + 1/9*108 + 1/9*99 + 1/9*98 + 1/9*95 + 1/9*90 + 1/9*85
= 98.3333
Filter
Simple 3*3 Neighbourhood
106
104
99
95
100
108
98
90
85
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
3*3 Smoothing Filter
104
100
108
99
106
98
95
90
85
Original Image Pixels
*
The above is repeated for every pixel in the original image to generate the smoothed image
Notes: 109

## Slide 110: Smoothing Spatial Filters
110
Box Filter all coefficients are equal
Weighted Average give more (less) weight to near (away from) the output location
Consider the output pixel is positioned at the center
Notes: 110

## Slide 111: Smoothing Filter: Example
111
original
3x3 average
Notes: 111

## Slide 112: Smoothing Filter: Example
112
original
3x3 average
Notes: 112

## Slide 113: Smoothing Filter: Example
113
original
3x3 average
Notes: 113

## Slide 114: Smoothing Filter: Example
114
original
3x3 average
Notes: 114

## Slide 115
115
Original image
Size: 500x500
Smooth by 3x3 box filter
Smooth by 5x5 box filter
Smooth by 9x9 box filter
Smooth by 15x15 box filter
Smooth by 35x35 box filter
Notice how detail begins to disappear
Notes: 115

## Slide 116: Order-Statistic Filtering
116
Output is based on order of gray levels in the masked area
Some simple neighbourhood operations include:
  Min: Set the pixel value to the minimum in the neighbourhood
  Max: Set the pixel value to the maximum in the neighbourhood
  Median: The median value of a set of numbers is the midpoint value in that set
Notes: 116

## Slide 117: Median Filtering
117
Median = ?
20
Particularly effective when
  The noise pattern consists of strong impulse noise ( salt-and-pepper)
Sort the values
Determine the median
Notes: 117

## Slide 118: Salt and Pepper Noise

## Slide 119: Median Filtering
119
Notes: 119

## Slide 120: Median Filtering
Original
Noisy

## Slide 121: Median Filtering
Noisy
Noisy

## Slide 122: Median Filtering
3x3-median x 1
3x3-blur x 1

## Slide 123: Median Filtering
3x3-median x 2
3x3-blur x 2

## Slide 124: Median Filtering
3x3-median x 5
3x3-blur x 5

## Slide 125: Median Filtering
3x3-median x 10
3x3-blur x 10

## Slide 126: Sharpening Spatial Filters
Previously we have looked at smoothing filters which remove fine detail
Sharpening spatial filters seek to highlight fine detail
  Remove blurring from images
  Highlight edges
Sharpening filters are based on spatial differentiation

## Slide 127: Spatial Differentiation
Let’s consider a simple 1 dimensional example

## Slide 128: Spatial Differentiation
A
B

## Slide 129: 1st Derivative
The 1st derivative of a function is given by:
Its just the difference between subsequent values and measures the rate of change of the function

## Slide 130
5 | 5 | 4 | 3 | 2 | 1 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 7 | 7 | 7 | 7
 | -1 | -1 | -1 | -1 | -1 | 0 | 0 | 6 | -6 | 0 | 0 | 0 | 1 | 2 | -2 | -1 | 0 | 0 | 0 | 7 | 0 | 0 | 0 | 
1st Derivative

## Slide 131: 2nd Derivative
The 2nd derivative of a function is given by:
Simply takes into account the values both before and after the current value

## Slide 132
5 | 5 | 4 | 3 | 2 | 1 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 7 | 7 | 7 | 7
2nd Derivative
 | -1 | 0 | 0 | 0 | 0 | 1 | 0 | 6 | -12 | 6 | 0 | 0 | 1 | 1 | -4 | 1 | 1 | 0 | 0 | 7 | -7 | 0 | 0 | 

## Slide 133: 2nd Derivative for Image Enhancement
The 2nd derivative is more useful for image enhancement than the 1st derivative - Stronger response to fine detail
We will come back to the 1st order derivative later on
The first sharpening filter we will look at is the Laplacian

## Slide 134: Laplacian Filter
The Laplacian is defined as follows:

## Slide 135: Laplacian Filter
So, the Laplacian can be given as follows:
0
1
0
1
-4
1
0
1
0
Can we implement it using a filter/ mask?

## Slide 136: Laplacian Filter

## Slide 137: Laplacian Filter
Applying the Laplacian to an image we get a new image that highlights edges and other discontinuities
Original Image
Laplacian Filtered Image
Laplacian Filtered Image Scaled for Display

## Slide 138: Laplacian Image Enhancement
The result of a Laplacian filtering is not an enhanced image
To generate the final enhanced image

## Slide 139: Laplacian Image Enhancement
In the final sharpened image edges and fine detail are much more obvious
-
=
Original Image
Laplacian Filtered Image
Sharpened Image

## Slide 140: Laplacian Image Enhancement

## Slide 141: Simplified Image Enhancement
The entire enhancement can be combined into a single filtering operation

## Slide 142: Simplified Image Enhancement
The entire enhancement can be combined into a single filtering operation
0
-1
0
-1
5
-1
0
-1
0

## Slide 143: Simplified Image Enhancement
This gives us a new filter which does the whole job for us in one step
0
-1
0
-1
5
-1
0
-1
0

## Slide 144: Use of first derivatives for image enhancement: The Gradient
The gradient of a function f(x,y) is defined as

## Slide 145: Use of first derivatives for image enhancement: The Gradient
The magnitude of this vector is given by:
For practical reasons this can be simplified as:

## Slide 146: Gradient Operators
There is some debate as to how best to calculate these gradients
Simplest Operator
x
y

## Slide 147: Gradient Operators
Prewitt Operator
-1 | -1 | -1
0 | 0 | 0
1 | 1 | 1
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
Extract horizontal edges
Extract vertical edges

## Slide 148: Gradient Operators
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
Extract horizontal edges
Emphasize more the current point (x direction)
Emphasize more the current point (y direction)
Pixel Arrangement
Extract vertical edges
Sobel Operator

## Slide 149: Sobel Operator: Example
Sobel filters are typically used for edge detection
An image of a contact lens which is enhanced in order to make defects more obvious

## Slide 150: Combining Spatial Enhancement Methods
Successful image enhancement is typically not achieved using a single operation
Rather we combine a range of techniques in order to achieve a final result
This example will focus on enhancing the bone scan

## Slide 151
Laplacian filter of bone scan (a)
Sharpened version of bone scan achieved by subtracting (a) and (b)
Sobel filter of bone scan (a)
(a)
(b)
(c)
(d)
Combining Spatial Enhancement Methods

## Slide 152
Combining Spatial Enhancement Methods
The product of (c) and (e) which will be used as a mask
Sharpened image which is sum of (a) and (f)
Result of applying a power-law trans. to (g)
(e)
(f)
(g)
(h)
Image (d) smoothed with a 5*5 averaging filter

## Slide 153
Combining Spatial Enhancement Methods
Compare the original and final images

## Slide 154: Acknowledgements
154
Digital Image Processing”, Rafael C. Gonzalez & Richard E. Woods, Addison-Wesley, 2002
Peters, Richard Alan, II, Lectures on Image Processing, Vanderbilt University, Nashville, TN, April 2008
Brian Mac Namee, Digitial Image Processing, School of Computing, Dublin Institute of Technology
Computer Vision for Computer Graphics, Mark Borg
Material in these slides has been taken from, the following resources
Notes: 154